## Slide 1: P&S Heterogeneous Systems Parallel Patterns: Reduction
Dr. Juan Gómez Luna
Prof. Onur Mutlu
ETH Zürich
Fall 2022
7 November 2022

## Slide 2: Performance Considerations

## Slide 3: Traditional Program Structure
CPU threads and GPU kernels
  Sequential or modestly parallel sections on CPU
  Massively parallel sections on GPU
Serial Code (host)
. . .
. . .
Parallel Kernel (device)
KernelA<<< nBlk, nThr >>>(args);
Serial Code (host)
Parallel Kernel (device)
KernelB<<< nBlk, nThr >>>(args);
Slide credit: Hwu & Kirk

## Slide 4: Memory Hierarchy in CUDA Programs

## Slide 5: Latency Hiding and Occupancy
FGMT can hide long latency operations (e.g., memory accesses)
Occupancy: ratio of active warps to the maximum number of warps per GPU core
4 active warps
2 active warps

## Slide 6: Memory Coalescing (I)
When threads in the same warp access consecutive memory locations in the same burst, the accesses can be combined and served by one burst
  One DRAM transaction is needed
  Known as memory coalescing
If threads in the same warp access locations not in the same burst, accesses cannot be combined
  Multiple transactions are needed
  Takes longer to service data to the warp
  Sometimes called memory divergence
Slide credit: Izzat El Hajj

## Slide 7: Memory Coalescing (II)
When accessing global memory, we want to make sure that concurrent threads access nearby memory locations
Peak bandwidth utilization occurs when all threads in a warp access one cache line (or several consecutive cache lines)
Md
Nd
W
I
D
T
H
WIDTH
Thread 1
Thread 2
Not coalesced
Coalesced
Slide credit: Hwu & Kirk

## Slide 8: Use Shared Memory to Improve Coalescing
Md
Nd
W
I
D
T
H
WIDTH
Md
Nd
Original
Access
Pattern
Tiled
Access
Pattern
Copy into
scratchpad
memory
Perform
multiplication
with scratchpad
values
Slide credit: Hwu & Kirk

## Slide 9: SIMD Utilization

## Slide 10: Threads Can Take Different Paths in Warp-based SIMD
Each thread can have conditional control flow instructions
Threads can execute different control flow paths
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B
C
D
E
F
A
G
Slide credit: Tor Aamodt

## Slide 11: Control Flow Problem in GPUs/SIMT
A GPU uses a SIMD pipeline to save area on control logic
  Groups scalar threads into warps
Branch divergence occurs when threads inside warps branch to different execution paths
Branch
Path A
Path B
Branch
Path A
Path B
Slide credit: Tor Aamodt
This is the same as conditional/predicated/masked execution.
Recall the Vector Mask and Masked Vector Operations?

## Slide 12: SIMD Utilization
Intra-warp divergence
Compute(threadIdx.x);
if (threadIdx.x % 2 == 0){
Do_this(threadIdx.x);
}
else{
Do_that(threadIdx.x);
}

## Slide 13: Increasing SIMD Utilization
Divergence-free execution
Compute(threadIdx.x);
if (threadIdx.x < 32){
Do_this(threadIdx.x * 2);
}
else{
Do_that((threadIdx.x%32)*2+1);
}

## Slide 14: Reduction Operation

## Slide 15: Reduction Operation
A reduction operation reduces a set of values to a single value
  Sum, Product, Minimum, Maximum are examples
Properties of reduction
  Associativity
  Commutativity
  Identity value
Reduction is a key primitive for parallel computing
  E.g., MapReduce programming model
Dean and Ghemawat, “MapReduce: Simplified Data Processing of Large Clusters,” OSDI 2004

## Slide 16: Sequential Reduction
A sequential implementation of reduction only needs a for loop to go through the whole input array
  N elements → N iterations
Many independent operations
  A parallel implementation can calculate multiple partial sums, and then reduce them
sum = 0; // Initialize with identity value
for(i = 0; i < N; ++i) {
sum += A[i]; // Accumulate elements of input array A[]
}

## Slide 17: Tree-Based Reduction
Iteration 1
Iteration 2
Iteration 3
Iteration 4
log(N) iterations
Partial results in temporary storage

## Slide 18: Tree-Based Reduction on GPU
Warp 0
Block 0
Block 1
Warp 1
Warp 0
Warp 1
Partial results in shared memory
(or registers)
Intra-block synchronization
__syncthreads();
Intra-block synchronization
__syncthreads();
Inter-block synchronization
Kernel termination and
  Final reduction on CPU, or
  Launch new reduction kernel on GPU
Atomic operations in global memory

## Slide 19: Vector Reduction: Naïve Mapping (I)
0
1
2
3
4
5
7
6
10
9
8
11
0+1
2+3
4+5
6+7
10+11
8+9
0...3
4..7
8..11
0..7
8..15
1
2
3
iterations
Thread 0
Thread 8
Thread 2
Thread 4
Thread 6
Thread 10
Slide credit: Hwu & Kirk
…

## Slide 20: Vector Reduction: Naïve Mapping (II)
Program with low SIMD utilization
  __shared__ float partialSum[]
  unsigned int t = threadIdx.x;
  for(int stride = 1; stride < blockDim.x; stride *= 2){
  __syncthreads();
  if (t % (2*stride) == 0)
  partialSum[t] += partialSum[t + stride];
  }
stride = 1
stride = 2
stride = 4
Warp 0
Warp 1
Warp 2
Warp 3
How to avoid the
warp underutilization?

## Slide 21: Divergence-Free Mapping (I)
All active threads belong to the same warp
Thread 0
0
1
2
3
…
13
15
14
18
17
16
19
0+16
15+31
1
2
3
Thread 1
Thread 2
Thread 14
Thread 15
iterations
Slide credit: Hwu & Kirk
…

## Slide 22: Divergence-Free Mapping (II)
Program with high SIMD utilization
  __shared__ float partialSum[]
  unsigned int t = threadIdx.x;
  for(int stride = blockDim.x; stride > 0; stride >> 1){
  __syncthreads();
  if (t < stride)
  partialSum[t] += partialSum[t + stride];
  }
stride = 16
stride = 8
stride = 4
Warp 0
Warp 1
Warp 2
Warp 3
Warp utilization
is maximized

## Slide 23: Divergence-Free Mapping (III)
Program with high SIMD utilization
  __shared__ float partialSum[]
  unsigned int t = threadIdx.x;
  for(int stride = blockDim.x; stride > 0; stride >> 1){
  __syncthreads();
  if (t < stride)
  partialSum[t] += partialSum[t + stride];
  }
stride = 16
stride = 8
stride = 4
Warp 0
Warp 1
Warp 2
Warp 3
We can use warp shuffle
to avoid
shared memory accesses
and __syncthreads()
stride = 2
stride = 1

## Slide 24: Warp Shuffle Functions
Built-in warp shuffle functions enable threads to share data with other threads in the same warp
  Faster than using shared memory and __syncthreads() to share across threads in the same block
Variants:
  __shfl_sync(mask, var, srcLane)
    Direct copy from indexed lane
  __shfl_up_sync(mask, var, delta)
    Copy from a lane with lower ID relative to caller
  __shfl_down_sync(mask, var, delta)
    Copy from a lane with higher ID relative to caller
  __shfl_xor_sync(mask, var, laneMask)
    Copy from a lane based on bitwise XOR of own lane ID
Slide credit: Izzat El Hajj

## Slide 25: Read and Write Access to GPU Shared Memory
    Threads running on processing engines have access to a local register file (LRF)
    And shared memory banks (SRF)
Nickolls et al., "Single Interconnect Providing Read and Write Access to a Memory Shared by Concurrent Threads," US7680988B1

## Slide 26: Read from Shared Memory Bank
Nickolls et al., "Single Interconnect Providing Read and Write Access to a Memory Shared by Concurrent Threads," US7680988B1

## Slide 27: Write to Shared Memory Bank
Nickolls et al., "Single Interconnect Providing Read and Write Access to a Memory Shared by Concurrent Threads," US7680988B1

## Slide 28: Shuffling Operations within a Warp
Nickolls et al., "Single Interconnect Providing Read and Write Access to a Memory Shared by Concurrent Threads," US7680988B1

## Slide 29: Divergence-Free Mapping (III)
Program with high SIMD utilization
  __shared__ float partialSum[]
  unsigned int t = threadIdx.x;
  for(int stride = blockDim.x; stride > 0; stride >> 1){
  __syncthreads();
  if (t < stride)
  partialSum[t] += partialSum[t + stride];
  }
stride = 16
stride = 8
stride = 4
Warp 0
Warp 1
Warp 2
Warp 3
We can use warp shuffle
to avoid
shared memory accesses
and __syncthreads()
stride = 2
stride = 1

## Slide 30: Tree-Based Reduction on GPU (with Warp Shuffle)
Warp 0
Block 0
Block 1
Warp 1
Warp 0
Warp 1
Partial results in shared memory
(or registers)
Intra-block synchronization
__syncthreads();
Warp
shuffle
__shfl_sync(…);
Inter-block synchronization
Kernel termination and
  Final reduction on CPU, or
  Launch new reduction kernel on GPU
Atomic operations in global memory

## Slide 31: Reduction with Warp Shuffle
__global__ void reduce_kernel(float* input, float* partialSums, unsigned int N) {
unsigned int segment = 2*blockDim.x*blockIdx.x;
unsigned int i = segment + threadIdx.x;
// Load data to shared memory
__shared__ float input_s[BLOCK_DIM];
input_s[threadIdx.x] = input[i] + input[i + BLOCK_DIM];
__syncthreads();
// Reduction tree in shared memory
for(unsigned int stride = BLOCK_DIM/2; stride > WARP_SIZE; stride /= 2) {
if(threadIdx.x < stride) {
input_s[threadIdx.x] += input_s[threadIdx.x + stride];
}
__syncthreads();
}
// Reduction tree with shuffle instructions
float sum;
if(threadIdx.x < WARP_SIZE) {
sum = input_s[threadIdx.x] + input_s[threadIdx.x + WARP_SIZE];
for(unsigned int stride = WARP_SIZE/2; stride > 0; stride /= 2) {
sum += __shfl_down_sync(0xffffffff, sum, stride);
}
}
// Store partial sum
if(threadIdx.x == 0) {
partialSums[blockIdx.x] = sum;
}
}
Slide credit: Izzat El Hajj

## Slide 32: Warp Reduce Functions
Ampere (cc 8.x) adds native support for warp-wide reduction operations
https://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html#warp-reduce-functions

## Slide 33: Tree-Based Reduction on GPU (with Warp Reduce)
Warp 0
Block 0
Block 1
Warp 1
Warp 0
Warp 1
Partial results in shared memory
(or registers)
Intra-block synchronization
__syncthreads();
Inter-block synchronization
Kernel termination and
  Final reduction on CPU, or
  Launch new reduction kernel on GPU
Atomic operations in global memory
Warp
reduce
__reduce_add_sync(…);

## Slide 34: Reduction with Warp Shuffle
__global__ void reduce_kernel(float* input, float* partialSums, unsigned int N) {
unsigned int segment = 2*blockDim.x*blockIdx.x;
unsigned int i = segment + threadIdx.x;
// Load data to shared memory
__shared__ float input_s[BLOCK_DIM];
input_s[threadIdx.x] = input[i] + input[i + BLOCK_DIM];
__syncthreads();
// Reduction tree in shared memory
for(unsigned int stride = BLOCK_DIM/2; stride > WARP_SIZE; stride /= 2) {
if(threadIdx.x < stride) {
input_s[threadIdx.x] += input_s[threadIdx.x + stride];
}
__syncthreads();
}
// Reduction tree with shuffle instructions
float sum;
if(threadIdx.x < WARP_SIZE) {
sum = input_s[threadIdx.x] + input_s[threadIdx.x + WARP_SIZE];
for(unsigned int stride = WARP_SIZE/2; stride > 0; stride /= 2) {
sum += __shfl_down_sync(0xffffffff, sum, stride);
}
}
// Store partial sum
if(threadIdx.x == 0) {
partialSums[blockIdx.x] = sum;
}
}
Slide credit: Izzat El Hajj

## Slide 35: Reduction with Warp Reduce
__global__ void reduce_kernel(int* input, int* partialSums, unsigned int N) {
unsigned int segment = 2*blockDim.x*blockIdx.x;
unsigned int i = segment + threadIdx.x;
// Load data to shared memory
__shared__ int input_s[BLOCK_DIM];
input_s[threadIdx.x] = input[i] + input[i + BLOCK_DIM];
__syncthreads();
// Reduction tree in shared memory
for(unsigned int stride = BLOCK_DIM/2; stride > WARP_SIZE; stride /= 2) {
if(threadIdx.x < stride) {
input_s[threadIdx.x] += input_s[threadIdx.x + stride];
}
__syncthreads();
}
// Reduction with warp reduce instruction
int sum;
if(threadIdx.x < WARP_SIZE) {
sum = input_s[threadIdx.x] + input_s[threadIdx.x + WARP_SIZE];
// Warp reduce intrinsic for cc 8.0 or higher
sum = __reduce_add_sync(0xffffffff, sum);
}
// Store partial sum
if(threadIdx.x == 0) {
partialSums[blockIdx.x] = sum;
}
}

## Slide 36: Atomic Operations (I)
CUDA provides atomic instructions on shared memory and global memory
  They perform read-modify-write operations atomically
Arithmetic functions
  Add, sub, max, min, exch, inc, dec, CAS
  int atomicAdd(int*, int);
Bitwise functions
  And, or, xor
Datatypes: int, uint, ull, float (half, single, double)*
Pointer to shared memory or global memory
Value to add
Return value (old value)
* Datatypes for different atomic operations in https://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html#atomic-functions

## Slide 37: Atomic Operations (II)
Atomic operations serialize the execution if there are atomic conflicts
tbase
tconflict
Shared memory
Shared memory
tbase
No atomic conflict = concurrent updates
Atomic conflict = serialized updates

## Slide 38: Recall: Uses of Atomic Operations
Computation
  Atomics on an array that will be the output of the kernel
  Example
    Histogram, reduction
Synchronization
  Atomics on memory locations that are used for synchronization or coordination
  Example
    Counters, locks, flags…
Use them to prevent data races when more than one thread need to update the same memory location

## Slide 39: Image Histogram
  Histograms are widely used in image processing
  Some computation before voting in the histogram may be needed
  Parallel threads frequently incur atomic conflicts in image histogram computation
For (each pixel i in image I){
  Pixel = I[i] // Read pixel
  Pixel’ = Computation(Pixel) // Optional computation
  Histogram[Pixel’]++ // Vote in histogram bin
}

## Slide 40: Optimized Parallel Reduction
7 versions in CUDA samples: Tree-based reduction in shared memory
  Version 0: No whole warps active
  Version 1: Contiguous threads, but many bank conflicts
  Version 2: No bank conflicts
  Version 3: First level of reduction when reading from global memory
  Version 4: Warp shuffle or unrolling of final warp
  Version 5: Warp shuffle or complete unrolling
  Version 6: Multiple elements per thread sequentially
https://docs.nvidia.com/cuda/cuda-samples/index.html#cuda-parallel-reduction
Harris, “Optimizing Parallel Reduction in CUDA,” https://developer.download.nvidia.com/assets/cuda/files/reduction.pdf

## Slide 41: 7 Versions of Reduction

## Slide 42: Reduction with Atomic Operations
3 new versions of reduction based on 3 previous versions
  Version 0: No whole warps active
  Version 3: First level of reduction when reading from global memory
  Version 6: Multiple elements per thread sequentially
New versions 7, 8, and 9
  Replace the for loop (tree-based reduction) with one shared memory atomic operation per thread

## Slide 43: 10 Versions of Reduction

## Slide 44: 10 Versions of Reduction
We save
lines of code

## Slide 45: Search Space of Parallel Reduction
Over 85 different versions possible!
Garcia de Gonzalo et al., “Automatic Generation of Warp-Level Primitives and Atomic Instructions for Fast and Portable Parallel Reduction on GPUs,” CGO 2019

## Slide 46: Automatic Generation of Parallel Reduction
Simon Garcia De Gonzalo, Sitao Huang, Juan Gomez-Luna, Simon Hammond, Onur Mutlu, and Wen-mei Hwu, "Automatic Generation of Warp-Level Primitives and Atomic Instructions for Fast and Portable Parallel Reduction on GPUs" Proceedings of the International Symposium on Code Generation and Optimization (CGO), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)]

## Slide 47: Parallel Reduction with Tensor Cores
Reduction can be expressed as a dot product operation and get accelerated by GPU tensor core units
  sum = A0 * B0 + A1 * B1 + … + AN-1 * BN-1
  With all Bi = 1, the result will be the sum of array A
Dakkak et al., “Accelerating Reduction and Scan Using Tensor Core Units,” ICS 2019

## Slide 48: Recommended Readings (I)
Hwu and Kirk, “Programming Massively Parallel Processors,” Third Edition, 2017
  Chapter 5: Performance considerations
  Chapter 9 - Parallel patterns —
  parallel histogram computation:
  An introduction to atomic operations
  and privatization

## Slide 49: Recommended Readings (II)
Hwu and Kirk and El Hajj, “Programming Massively Parallel Processors,” Fourth Edition, 2022
  Chapter 6 - Performance considerations
  Chapter 10 - Reduction: And
  minimizing divergence

## Slide 50: P&S Heterogeneous Systems Parallel Patterns: Reduction
Dr. Juan Gómez Luna
Prof. Onur Mutlu
ETH Zürich
Fall 2022
7 November 2022